## Slide 1
1
NAME: FORM/GROUP
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2017 V.Ryan © 2017
This booklet can be duplicated and printed. Individual pages can be removed if they are not required.
Editing of text / images is NOT allowed.
The links to www.technologystudent.com cannot be removed.
The PDF ﬁle can be stored on school / college systems and distributed electronically (NO EDITING ALLOWED)
PLEASE RESPECT THE COPYRIGHT - report infringers to techteacher@technologystudent.com
EQUIPMENT AND TOOLS WORKBOOK
THE G CRAMP
THE BENCH DRILL
SASH CLAMPS
THE FRETSAW DRILLING MACHINES
THE HAND DRILL
TYPES OF PLANE
THE MARKING GAUGE THE SLIDING BEVEL
THE WOODWORKERS TRY-SQUARE
THE ENGINEERS TRY-SQUARE BACK SAWS THE COPING SAW
THE HACKSAW
CHISELS THE DISK SANDER
THE CENTRE PUNCH AND DOT PUNCH
THE HOT GLUE GUN THE HAND FILE SEQUENCE DRAWING - VACUUM FORMING
THE STRIP HEATER
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 2: RECORD SHEET
EQUIPMENT / TOOL | DATE
THE FRETSAW | 
DRILLING MACHINES | 
THE BENCH DRILL | 
THE HAND DRILL | 
THE G CRAMP | 
SASH CLAMPS | 
TYPES OF PLANE | 
THE WOODWORKERS TRY-SQUARE | 
THE MARKING GAUGE | 
THE ENGINEERS TRY-SQUARE | 
THE SLIDING BEVEL | 
BACK SAWS - TENON SAWS AND DOVETAIL SAWS | 
THE COPING SAW | 
THE HACKSAW | 
THE CENTRE PUNCH AND DOT PUNCH | 
CHISELS | 
THE HOT GLUE GUN | 
THE HAND FILE | 
THE DISK SANDER | 
SEQUENCE DRAWING - VACUUM FORMING | 
THE STRIP HEATER | 
Record the completion date of each worksheet.
Use the web links on each of the sheets, for information and guidance.
www.technologystudent.com © 2017 V.Ryan © 2017
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/

## Slide 3
1. The Fretsaw is a general workshop machine. What materials can be cut and shaped using this machine?
ON
OFF
3. Describe how the machine can be operated safely.
ON
OFF
Look carefully at the fretsaw seen below. What is wrong with the way it has been left for the next user/operator?
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
THE FRETSAW
2. Label the parts of the fretsaw identiﬁed by the arrows on the diagram below.
HELPFUL LINK https://www.technologystudent.com/equip1/fretsw1.htm
www.technologystudent.com © 2017 V.Ryan © 2017
V.Ryan © 2018
V.Ryan © 2018

## Slide 4
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
DRILLING MACHINES
1. Two common types of drilling machine are seen below. Name both types.
NAME:
NAME:
2. Label the ‘arrowed’ parts.
3. The main diﬀerence between the two machine drills is their overall size. Why is one much smaller than the other? Include a description of the type of work normally carried out on the smaller drill, as part of your
answer.
4. List four safety rules governing the use of drilling machines.
HELPFUL LINK https://www.technologystudent.com/equip1/macdrl1.htm
www.technologystudent.com © 2017
V.Ryan © 2017

## Slide 5
DRILLING MACHINES - CONTINUED
5. Three types of drill bit are seen below. Name each ‘bit’ and write a general description of the type of drilling each is capable of producing, when used in conjunction with a drilling machine.
DRILL BIT NAME:
TYPICAL USE:
DRILL BIT NAME:
TYPICAL USE:
DRILL BIT NAME:
TYPICAL USE:
6. The machine drill shown opposite is being used in a very dangerous manner. Identify and describe all the dangers.
HELPFUL LINK https://www.technologystudent.com/equip1/macdrl1.htm
www.technologystudent.com © 2017 V.Ryan © 2017
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
V.Ryan © 2018

## Slide 6
THE BENCH DRILL
https://www.facebook.com/groups/254963448192823/
HELPFUL LINK https://www.technologystudent.com/equip_ﬂsh/hdrill4.html
www.technologystudent.com © 2017 V.Ryan © 2017
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
V.Ryan © 2018
1. Complete the diagram of the bench drill, seen opposite. Label the important parts. Add appropriate colour and shade.
2. Add safety information in the space below. You may wish to explain the use of the guard or how work must be safely
clamped before being drilled.
SAFETY INFORMATION:

## Slide 7
THE HAND DRILL
1. Complete this worksheet by adding labels to the diagram shown below.
HELPFUL LINKS: https://www.technologystudent.com/equip1/hdrill1.htm
https://www.technologystudent.com/equip1/drilly.htm
V.Ryan © 2018

## Slide 8
THE HAND DRILL
HELPFUL LINKS: https://www.technologystudent.com/equip1/hdrill1.htm https://www.technologystudent.com/equip1/drilly.htm
2. The sequence of drawings, show the use of a hand drill. Add notes to each stage.
BIT
HAND DRILL
CHUCK
MASKING TAPE
MASKING TAPE MARKS CORRECT DEPTH
MASKING TAPE
CHUCK
MASKING TAPE
MARKS CORRECT
DEPTH
www.technologystudent.com © 2017 V.Ryan © 2017
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
V.Ryan © 2018
V.Ryan © 2018
V.Ryan © 2018

## Slide 9
THE G CRAMP
https://www.facebook.com/groups/254963448192823/
WINGNUT
TOMMY BAR
1. In order to tighten a G Cramp, a tommy bar is turned in a clockwise direction. Some G cramps have a wing nut in place of the tommy bar.
Draw a typical wing nut in the box (below).
2. Add the missing labels to the diagram of the G cramp.
3. List two other types of clamps and brieﬂy describe how they are used.
CLAMP NAME:
HOW USED:
CLAMP NAME:
HOW USED:
HELPFUL LINK https://www.technologystudent.com/equip1/cramp1.htm
www.technologystudent.com © 2017 V.Ryan © 2017
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
V.Ryan © 2018

## Slide 10
THE G CRAMP
https://www.facebook.com/groups/254963448192823/
HELPFUL LINK https://www.technologystudent.com/equip1/cramp1.htm
www.technologystudent.com © 2017
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
V.Ryan © 2017
4. A ﬂat piece of MDF has been placed on the table of the bench drill shown below. The MDF needs securing to the table for safety reasons.
Draw the G cramp in the correct position.
V.Ryan © 2018
5. What are the dangers of holding the work in the hand whilst drilling?

## Slide 11
1. Label the parts of the sash clamp shown below.
SASH CLAMPS
https://www.facebook.com/groups/254963448192823/
2. The box (below) is to be held together with sash clamps. On the diagram, draw a sash clamp in the correct position, across the box. Add explanatory notes.
NOTES:
3. Scrap wood is normally placed either side of the item to be clamped. Why is this the case?
4. Sash clamps are available in a range of lengths. What is the range?
5. The parts of a sash clamp are manufactured from suitable materials. What are the materials?
6. Why is the sash clamp tightened with a tommy bar?
HELPFUL LINK https://www.technologystudent.com/equip1/sash1.htm
www.technologystudent.com © 2017 V.Ryan © 2017
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
V.Ryan © 2018

## Slide 12
7. The box shown below is held together with sash clamps, whilst the glue dries. It is vital that each corner of the box is an accurate 90 degree angle. Two basic tools are used to check that the angles are correct.
Name each tool.
Describe the use of each tool
Draw each tool on the diagram below, showing each one in use.
TOOL 1: DESCRIPTION OF USE:
TOOL 2:
DESCRIPTION OF USE:
V.Ryan © 2018
SASH CLAMPS
https://www.facebook.com/groups/254963448192823/
HELPFUL LINK https://www.technologystudent.com/equip1/sash1.htm
www.technologystudent.com © 2017 V.Ryan © 2017
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS

## Slide 13
TYPES OF PLANE
https://www.facebook.com/groups/254963448192823/
The planes seen below are regularly used in a workshop. Add the name of each plane and include notes explaining the purpose of each one.
NAME:
PURPOSE:
NAME:
PURPOSE:
NAME:
PURPOSE:
NAME:
PURPOSE:
HELPFUL LINK https://www.technologystudent.com/equip1/planes1.htm
www.technologystudent.com © 2017 V.Ryan © 2017
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS

## Slide 14
TYPES OF PLANE - CONTINUED
The planes seen below are regularly used in a workshop. Add the name of each plane and include notes explaining the purpose of each one.
NAME:
PURPOSE:
NAME:
PURPOSE:
NAME:
PURPOSE:
NAME:
PURPOSE:
www.technologystudent.com © 2017 V.Ryan © 2017
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
HELPFUL LINK https://www.technologystudent.com/equip1/planes1.htm

## Slide 15
MARKING KNIFE
THE WOODWORKERS TRY-SQUARE
TRY-SQUARE
WOOD
A typical woodworkers try square is shown opposite.
STOCK
BRASS FACE
The blade is manufactured from:
BLADE
The blade has been hardened and tempered because:
3. Why does the stock have a brass face?
A try square and marking knife are used to mark out lengths of wood to the correct distance. Draw the marking knife in the correct position on the diagram shown opposite.
Why is a marking knife used rather than a pencil. Two possible answers are written below. Put a tick in the box opposite the correct answer.
The knife cuts/breaks precisely, the wood ﬁbres. This means that when a saw is used to cut away the waste wood, a frayed or uneven edge is avoided.
A pencil requires sharpening and this slows down the marking out procedure.
The diagram opposite shows a woodworkers try square being used to carry out an important quality check.
Explain / describe the quality check.
LIGHT SHINES THROUGH GAP
Describe another use of a woodworkers try square. Include a sketch.
HELPFUL LINK https://www.technologystudent.com/equip1/try1.htm
www.technologystudent.com © 2017 V.Ryan © 2017
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
V.Ryan © 2018
V.Ryan © 2018
V.Ryan © 2018

## Slide 16
THE MARKING GAUGE
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
A typical marking gauge is seen opposite. Complete the diagram by adding the missing labels.
Add appropriate colour and shade to the diagram.
What is the function of the marking gauge?
4. What materials are used for the manufacture of the various parts of the marking gauge?
5. Look carefully at the diagram of the marking gauge being used.
Describe what is happening in the diagram?
6. Below is a description of how the distance between the spur and the stock is set:
“The distance between the stock and the spur can be adjusted by loosening the thumbscrew which allows the stock to slide along the stem. The thumbscrew can then be tightened, once the correct distance has been reached. A ruler is used to set the distance”.
In the space opposite, draw a diagram that represents the description written above.
HELPFUL LINK https://www.technologystudent.com/equip1/mgauge1.htm
www.technologystudent.com © 2017
V.Ryan © 2017
V.Ryan © 2018
V.Ryan © 2018

## Slide 17
THE ENGINEERS TRY-SQUARE
BLADE
STOCK
What material is used to manufacture an engineers try square?
The blade is specially treaded. What is this treatment called?
3. Why is the blade treated in this special way?
ENGINEERS TRY-SQUARE
TRY-SQUARE
1. A typical engineers try square is shown opposite. How does it diﬀer from a typical woodworkers try square?
4. A try square and another engineers tool are used to mark out metals.
Label this second tool (shown on the diagram).
Describe the marking out procedure.
5. An engineers try square has been designed to include a small slot, as indicated on the diagram shown opposite. Why is this slot
essential?
HELPFUL LINK https://www.technologystudent.com/equip1/try2.htm
www.technologystudent.com © 2017 V.Ryan © 2017
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
V.Ryan © 2018
V.Ryan © 2018
V.Ryan © 2018
STEEL
6. Describe another typical use of an engineers try square. Include a sketch. SKETCH NOTES

## Slide 18
THE SLIDING BEVEL
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
STOCK
BLADE
hardened and tempered stock
locked blade
1. The diagram shows an incomplete sliding bevel. Complete the diagram by:
Adding the missing parts.
Adding appropriate colour and shade. (consider the materials used to manufacture this tool).
rosewood sliding bevel angle
2. The paragraph below describes the siding bevel. Some of the words are missing. Fill in the missing words (they are displayed below the paragraph).
The is composed of two parts, the and the . The stock is usually made from which is a high quality material. The blade is made from steel. The blade can be adjusted to a variety of and in position. This is useful when a line has to be marked at an on wood.
angles
LOCK LOOSENED
THE LOCK ON THE SLIDING BEVEL IS TIGHTENED SO THAT THE
ANGLE OF THE BLADE CANNOT BE ALTERED ACCIDENTALLY. A MARKING KNIFE IS USED TO MARK A LINE AT THE CORRECT ANGLE.
3. Complete the two stages of using a sliding bevel, by adding text / notes and a diagram.
ADD YOUR TEXT HERE:
ADD YOUR DIAGRAM HERE
1
2
HELPFUL LINK https://www.technologystudent.com/equip1/bevel1.htm
www.technologystudent.com © 2017 V.Ryan © 2017
V.Ryan © 2018

## Slide 19
BACK SAWS - TENON SAWS AND DOVETAIL SAWS
1. Complete the diagram of the tenon saw shown below. Add the three missing labels and appropriate add colour and shade.
2. All back saws, such as a typical tenon saw or dovetail saw have a brass back. Why is this the case?
INDEX FINGER
3. A typical tenon saw is shown opposite. Complete the drawing by adding a hand. Your drawing should clearly show how a back saw should be held, and in particular, the position
of the index ﬁnger.
4. Tenon saws and dovetail saws are used for slightly diﬀerent cutting/sawing. Describe the type of cutting for each saw.
TENON SAW:
DOVETAIL SAW:
5. The diagram opposite shows a piece of wood, a bench hook and tenon saw. Describe the sawing technique.
HELPFUL LINK https://www.technologystudent.com/equip1/bksaw1.htm
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2017 V.Ryan © 2017
V.Ryan © 2018
V.Ryan © 2018

## Slide 20
THE COPING SAW
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
1. Complete the diagram of the coping saw shown below. Add the three missing labels and appropriate add colour and shade.
2. The coping saw blade must face in the correct position. Write an explanation below.
3. Explain how a new blade is secured to the frame of a coping saw. Use notes and a sketch to aid your explanation.
SKETCH NOTES
4. Coping saws are ideal for cutting internal shapes/curves. The incomplete diagram below, shows the procedure for this type of cutting. Complete the diagram and add explanatory notes.
SHAPE TO BE CUT
NOTES
HELPFUL LINK https://www.technologystudent.com/equip1/coping1.htm
www.technologystudent.com © 2017 V.Ryan © 2017
V.Ryan © 2018
DIAGRAM

## Slide 21
THE HACKSAW
1. What materials are cut to size / shape using a hacksaw?
2. Why are hacksaws adjustable (sometimes hacksaws are referred to as adjustable hacksaws)?
3. What is meant by the abbreviation TPI ? Explain your answer.
4. Complete the table below. This refers to teeth per inch (25mm) and the type of material each hacksaw blade is most suited to cut.
TEETH PER INCH (25mm) | SUITABLE FOR CUTTING
14 TPI | 
18 TPI | 
24 TPI | 
32 TPI | 
5. Complete the diagram of the adjustable hacksaw by:
Adding the missing parts.
Adding the names of the identiﬁed parts.
6. Explain how the blade of a hacksaw is changed. You should also explain the direction in which the teeth of the blade should point if the blade is correctly set up.
HELPFUL LINK https://www.technologystudent.com/equip_ﬂsh/hacksw1.html
www.technologystudent.com © 2017 V.Ryan © 2017
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
V.Ryan © 2018

## Slide 22
THE CENTRE PUNCH AND DOT PUNCH
1. In the space below, draw diagrams of a centre punch and dot punch. Underneath each sketch, add notes describing each of the tools.
CENTRE PUNCH DOT PUNCH
y
a
n
R
.
V
y
B
BALL PEIN HAMMER
CENTRE PUNCH
MATERIAL
3. If a centre punch is not used to mark the position of a hole before drilling, what could be an undesirable outcome?
2. The diagram opposite, shows one use of a centre punch. Add a description, alongside the diagram.
HELPFUL LINK https://www.technologystudent.com/equip1/punch1.htm
www.technologystudent.com © 2017
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
V.Ryan © 2017
V.Ryan © 2018
NOTES
NOTES

## Slide 23
CHISELS
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
CHISEL
BENCH TOP
G CRAMP
4. Three cross sections of three common chisels are shown below. Write the name of each chisel, underneath the correct section.
A B C
BENCH OTP
1. Diagrams ‘A’ and ‘B’ show two ways of using a chisel incorrectly. Describe what is wrong.
A
B
DIAGRAM A:
DIAGRAM B:
2. A blunt chisel can be more dangerous than sharp chisel. Why is this the case?
3. The diagram opposite shows the correct use of a chisel.
Describe the technique and explain the safety precautions shown in the diagram.
The handles of most chisels are manufactured from:
Why should both hands be kept behind the cutting edge when using a chisel?
HELPFUL LINK https://www.technologystudent.com/equip1/chisels.htm
www.technologystudent.com © 2017
V.Ryan © 2017
V.Ryan © 2018
V.Ryan © 2018
V.Ryan © 2018

## Slide 24
THE HOT GLUE GUN
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
1. A hot glue gun is shown below. Complete the diagram by adding the missing labels.
2. Explain how the glue gun shown above works.
3. Complete the diagram of the hot glue gun shown below. Add suitable colour and shade.
4. What safety factors should be kept in mind when using a hot glue gun?
5. What type of work is a hot glue gun best suited to ‘glue’ together?
HELPFUL LINK https://www.technologystudent.com/equip1/htglu1.htm
www.technologystudent.com © 2017
V.Ryan © 2017
V.Ryan © 2018

## Slide 25
THE HAND FILE
https://www.facebook.com/groups/254963448192823/
2. Why is high carbon steel used for the manufacture of the main part of the ﬁle?
3. With the aid of a diagram, explain the technique called ‘through ﬁling’. DRAWING NOTES
4. The drawing below shows another ﬁling technique. Name and describe the technique.
TECHNIQUE NAME:
DESCRIPTION:
5. With the aid of a sketch / diagram, explain the importance of a ‘safe edge’.
DRAWING NOTES
HELPFUL LINKS https://www.technologystudent.com/equip1/hﬁle1.htm https://www.technologystudent.com/equip1/hﬁle2.htm
1. A typical hand ﬁle is shown below. Add the labels, as indicated by the arrows.
www.technologystudent.com © 2017
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
V.Ryan © 2017
V.Ryan © 2018

## Slide 26
ON
OFF
THE DISK SANDER
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
1. Complete the labels on the diagram of the disk sander, shown opposite.
2. List safety precautions that need to be applied when using the disk sander?
3. Draw a simple version of a disk Sander and identify all its dangers.
4. Why is it important to wear a dust mask and to use extraction, when using a sanding disk?
HELPFUL LINK https://www.technologystudent.com/equip_ﬂsh/disker2.html
www.technologystudent.com © 2017
V.Ryan © 2017
V.Ryan © 2018

## Slide 27
THE MOULD IS PLACED IN THE FORMER
HEATER
THE AIR IS OUT OF THE AREA BELOW THE PLASTIC AND MOULD.
HEATER
THE PLASTIC BECOMES
WHEN HEATED
THE ELECTRIC IS TURNED ON TO WARM THE PLASTIC SHEET.
HEATER
V.Ryan © 2018
HEATER
SHEET IS PLACED ABOVE THE MOULD AND
SECURELY.
Complete the sequence drawing below by adding the missing words and parts of each diagram.
Add colour / shade.
1. 2.
HEATER
A SUITABLE
IS CAREFULLY MANUFACTURED
SEQUENCE DRAWING - VACUUM FORMING
3.
4.
5.
6.
HELPFUL LINK https://www.technologystudent.com/equip1/vacform1.htm
www.technologystudent.com © 2017 V.Ryan © 2017
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/

## Slide 28
THE STRIP HEATER
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
Draw a series of small diagrams, representing the stages of vacuum forming,
Add an explanation of each stage on the right hand side. The ﬁrst stage has already been included
STAGE ONE: The position of the fold is marked with a china-graph pencil. With this type of pencil the line can be removed easily later.
www.technologystudent.com © 2017
V.Ryan © 2017
HELPFUL LINK
https://www.technologystudent.com/equip1/stques1.htm https://www.technologystudent.com/joints/desk17.htm